## Slide 1: Module 00109 Introduction to Material Handling
Copyright © 2021 by NCCER, Alachua, FL 32615. Published by Pearson. All rights reserved.

## Slide 2: 1.0.0 Material Handling

## Slide 3: Objective
Successful completion of this module prepares you to do the following:
Identify the basic concepts of material handling and common safety precautions.
  Describe the basic concepts of material handling and manual lifting.
  Identify common material handling safety precautions.
  Identify and describe how to tie knots commonly used in material handling.

## Slide 4: Performance Tasks
Under supervision, you should be able to do the following:
Demonstrate safe manual lifting techniques.
Demonstrate how to tie two of the following common knots:
  Square
  Bowline
  Half hitch
  Clove hitch
  k
  dx
Module 00109 – Introduction to Material Handling

## Slide 5: Trade Terms (1 of 2)
Square knot: A knot made of two reverse half-knots and typically used to join the ends of two ropes of similar diameters; also called a reef knot.
Bowline: A knot used to form a loop that neither slips nor jams; sometimes referred to as a rescue knot or the king of knots.
Half hitch: A knot tied by passing the working end of a rope around an object, across the standing part of the rope, and then through the resulting loop; often used as an element in forming other knots or added to make other knots more secure.
Module 00109 – Introduction to Material Handling

## Slide 6: Trade Terms (2 of 2)
Clove hitch: A knot that consists of two half hitches made in opposite directions; used to temporarily secure a rope to an object.
Standing end: The end of a rope that is not being knotted.
Working end: The end of a rope that is being used to tie a knot.
Standing part: The portion of a rope that is between the standing end and the working end.
Capsize: To change the form and rearrange the parts of a knot, usually by pulling on specific ends of the knot.
Module 00109 – Introduction to Material Handling

## Slide 7: 1.1.0 – Material Handling Basics
To prevent injuries when handling materials:
Pre-plan the task.
Wear appropriate PPE.
Follow proper lifting procedures.
Be aware of hazards posed by heights and suspended loads.

## Slide 8: 1.1.1–1.1.2 – Pre-Task Planning and Personal Protective Equipment
Basic Guidelines
Assess the situation before attempting a lift.
Wear the proper clothing.
Use the appropriate PPE.
Follow established policies.

## Slide 9: 1.1.3 – Proper Lifting and Lowering Procedures (1 of 2)
Safe Lifting Technique

## Slide 10: 1.1.3 – Proper Lifting and Lowering Procedures (2 of 2)
Guidelines for Lowering a Load
Size up the load first.
Lower the load in the same way it would be lifted.
Treat the area that the load is being lowered into as a fall zone.

## Slide 11: 1.2.1 – Stacking and Storing Materials (1 of 3)
Follow safety guidelines for stacking and storing items such as:
Cartons
Lumber
Pipes
Items that should be chocked
Items that should be tied down or banded
Bags
Bricks
Masonry blocks
Flammable materials
Always properly store materials and equipment when they are not in current use

## Slide 12: 1.2.1 – Stacking and Storing Materials (2 of 3)
Stack loose bricks no higher than seven feet (2.1 m). Above four feet (1.2 m), begin stacking two inches (5 cm) in from the edge, continuing in this manner for each additional foot of height up to seven feet (2.1 m).

## Slide 13: 1.2.1 – Stacking and Storing Materials (3 of 3)
A stack of masonry blocks is set back one-half block per layer above six feet (1.8 m).

## Slide 14: 1.2.2 – Working from Heights
Safety Guidelines
Use a safety harness with a fall-arrest lanyard at heights over 6 feet (2 m).
Use a rope to raise or lower tools and materials.
Tie off tools and materials to keep them secured in elevated work areas.
Follow precautions to use ladders safely.
Never stack or store materials on scaffolds or runways.

## Slide 15: 1.3.0 – Knots for Material Handling
Knots and Hitches
True knots must be unwoven to be unfastened.
Hitches can be undone by pulling in the reverse direction from that in which the knots are meant to hold.
Key knot-tying terms are: standing end, working end, standing part, and capsize.

## Slide 16: 1.3.1 – The Square Knot (1 of 2)

## Slide 17: 1.3.1 – The Square Knot (2 of 2)
The granny knot is the result if the second half knot is tied in the wrong direction when tying a square knot. It is a highly insecure knot!

## Slide 18: 1.3.2 – The Bowline
Do not use this knot if the rope may have to be released while under load!

## Slide 19: 1.3.3 – The Half Hitch
Do not use this knot alone for heavy loads or when safety is critical!

## Slide 20: 1.3.4 – The Clove Hitch (1 of 3)
Do not use this knot alone; use additional half hitches to make it more secure.
Threading the End Technique

## Slide 21: 1.3.4 – The Clove Hitch (2 of 3)
Stacked Loops Technique

## Slide 22: 1.3.4 – The Clove Hitch (3 of 3)
Two Half Hitches Technique

## Slide 23: 1.0.0 Section Review Question One
Loose clothing is best to wear when handling material.
True
False

## Slide 24: 1.0.0 Section Review Question One Answer
Loose clothing is best to wear when handling material.
True
False

## Slide 25: 1.0.0 Section Review Question Two
All of these are proper lifting technique except ________.
bend your knees
lift with your legs
keep you back straight
keep your head down

## Slide 26: 1.0.0 Section Review Question Two Answer
All of these are proper lifting technique except ________.
bend your knees
lift with your legs
keep you back straight
keep your head down

## Slide 27: 1.0.0 Section Review Question Three
Only store materials and equipment when they will not be in use for a week or more.
True
False

## Slide 28: 1.0.0 Section Review Question Three Answer
Only store materials and equipment when they will not be in use for a week or more.
True
False

## Slide 29: 1.0.0 Section Review Question Four
A knot used to form a loop that neither slips nor jams is called a ________.
bow knot
clove hitch
bowline
square knot

## Slide 30: 1.0.0 Section Review Question Four Answer
A knot used to form a loop that neither slips nor jams is called a ________.
bow knot
clove hitch
bowline
square knot

## Slide 31: 1.0.0 Section Review Question Five
Ask a co-worker for assistance when an object is longer than ________.
8 feet
10 feet
12 feet
15 feet

## Slide 32: 1.0.0 Section Review Question Five Answer
Ask a co-worker for assistance when an object is longer than ________.
8 feet
10 feet
12 feet
15 feet

## Slide 33: Next Section… 2.0.0 Material Handling Equipment Read Sections 2.0.0 through 2.2.6. Complete the Section 2.0.0 Section Review.